Name ________________________					Date _________________________

Intro to Physics								Circuits WS #2

Period _____________							Mrs. Nadworny

Ohm’s Law

Directions: Solve the following problems using the GUESS method and proper significant figures. Be sure to show ALL work.

- Which graph best represents the relationship between the potential difference across a conductor and the current through the conductor at constant temperature?

| (A) |  | (B) |  | (C) |  | (D) |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

- A prototype electric car is powered by a 312 V battery pack. What is the resistance of the motor circuit when 78 A of current flows through the circuit?

Givens:			Write Equation: 			Substitute:		Solution with units:

R = ?

V =

I =

- A team from Texas A&M University has built an electric sports car with an enormous maximum motor current. Determine this current if it can be provided by a 720 V power supply and the circuit resistance is 0.30 Ω.

Givens:			Write Equation: 			Substitute:		Solution with units:

R =

V =

I = ?

- When a 62 Ω resistor is connected to a battery, the current in the circuit is 0.39 A. What is the potential difference of the battery?

Givens:			Write Equation: 			Substitute:		Solution with units:

R =

V = ?

I =

- A circuit has a 45.0 volt battery connected to a resistor. There is 0.150 amperes of current flowing through the circuit.  What is the resistance of the of the resistor?

Givens:			Write Equation: 			Substitute:		Solution with units:

R = ?

V =

I =

- A circuit has a 3.50 volt battery connected to a 47 ohm resistor. Calculate the current flowing through the circuit.

Givens:			Write Equation: 			Substitute:		Solution with units:

R =

V =

I = ?

- When a 150 Ω resistor is connected to a battery, the current in the circuit is 0.75 A. What is the potential difference of the battery?

Givens:			Write Equation: 			Substitute:		Solution with units:

R =

V = ?

I =